## Slide 1: PPP Survey PPP Execution Example
Term project #1

## Slide 2: Setting Virtual Machine
Set up serial port in virtual machine
  Need 2 VMs for communicate

## Slide 3: Serial Port Set Up in VM1
- 포트/파일 경로: \\.\pipe\com1으로 설정(1: 포트번호)
ex) 포트번호를 COM1로 설정, 포트/파일 경로 \\.\pipe\com1 로 설정
- vm1은 존재하는 파이프/소켓에 연결 체크 안함, vm2는 체크
- virtual machine 실행 시 존재하는 파이프/소켓에 연결을 체크하지 않은 vm부터 실행시켜야함
(즉 이 예제에선 vm1부터 실행시켜야 vm이 모두 켜짐)

## Slide 4: Serial Port Set Up in VM2

## Slide 5: What is a Null Modem.
Null modem is a communication method to connect two DTEs
(computer, terminal, printer etc.) directly
using an RS-232 serial cable.

## Slide 6: Null modem in virtual machine

## Slide 7: PPP Connection
Check PPP applications
$ which pppd
$ which pppdump
Install : # apt-get install ppp

## Slide 8: pppd connection
Command format
  Local IP : My IP address
  Remote IP : Correspond IP address
  ttyname : /dev/ttySx (x : port number)
  record <path> : full path (ex : /root/test01)
  Speed : 38400 (bps)
# pppd -detach crtscts lock debug record <path> noccp <local IP>:<remote IP> ttyname speed

## Slide 9: ttySx mapping
# setserial –g /dev/ttyS*

## Slide 10: pppd command option
Command option
- option ($man pppd)
· crtscts: specifies that pppd should set the serial port to use h/w flow control.
· lock: specifies that pppd should create a UUCP-style lock file for the serial device
to ensure exclusive access to the device. By default, pppd will not create a lock
· debug: Enables connection debugging facilities. If this option is given, pppd will log the
contents of all control packets sent or received in a readable form.
· record <path>: Specifies that pppd should record all characters sent and received to
path
· <local IP>:<remote IP>: Set the local and/or remote interface Ip address.
· ttyname: Use the serial port called ttyname to communicate with the peer.
· speed: An option that is a decimal number is taken as the desired baud rate for the
serial device.
# pppd -detach crtscts lock debug record <path> noccp noaccomp nopcomp asyncmap 0xffffffff <local IP>:<remote IP> ttyname speed

## Slide 11: pppd command option
· noccp: disable CCP(Compression Control protocol) negotiation.
· noaccomp: Disable Address/Control compression in both directions (send and receive).
· nopcomp: Disable protocol field compression negotiation in both the receive and the
transmit direction.
· asyncmap <map>: This option sets the Async-Control-Character-Map (ACCM) for this end of the link. The ACCM is a set of 32 bits, one for each of the ASCII control characters with values from 0 to 31, where a 1 bit indicates that the corresponding control character should not be used in PPP packets sent to this system. The map is encoded as a hexadecimal number (without a leading 0x) where the least significant bit (00000001) represents character 0 and the most significant bit (80000000) represents character 31. Pppd will ask the peer to send these characters as a 2-byte escape sequence. If multiple asyncmap options are given, the values are ORed together. If no asyncmap option is given, the default is zero, so pppd will ask the peer not to escape any control characters. To escape transmitted characters, use the escape option.

## Slide 12: pppd connection command
pppd execution
  Terminal1 (VM1)
  Terminal2 (VM2)
    Same as terminal1, only swap local IP for remote IP
  record /root/test01 : Set the path for dump file
# pppd -detach crtscts lock debug record /root/test02 noccp 10.1.3.20:10.1.3.10 /dev/ttyS0 38400
# pppd -detach crtscts lock debug record /root/test02 noccp 10.1.3.10:10.1.3.20 /dev/ttyS0 38400

## Slide 13: pppd connection example - debug

## Slide 14: PPP frame analysis
Dump file output
#pppdump –h <path>
  The pppdump utility converts the files written using the record option of pppd into a human-readable format.

## Slide 15
pppdump
default option

## Slide 16
pppdump with
noaccomp,
nopcomp,
asyncmap 0xffffffff
options

## Slide 17: HDLC PPP LCP frame example

## Slide 18: Frame Delimiter
Frame delimiter (flag)
  A frame delimiter marks the end of one frame and the beginning of another. A frame delimiter at the end of a frame may also mark the start of the next frame.
  The next frame is after an idle period
  In case of continuous communication

## Slide 19: Homework #1
PPP survey
  submit a report of PPP with reference to RFC documents. (+PPP.pdf)
  The report must include contents of RFC 1661 (PPP LCP), RFC 1662 (HDLC) and RFC 1332 (IPCP).

## Slide 20: Homework #1
pppd execution
  Execute pppd following this documents.
    Execute twice: First one executes default option, and other is with noaccomp, nopcomp, asyncmap 0xffffffff option
  Send a ping from terminal1 to terminal2 when the connection is established.
    Ex) $ ping –c 2 10.1.3.20 (correspond IP address)
submission
  Result screenshot
    Execution results, debug option on, dump output
      both of default option and noaccomp,… option.
  Report
    Explain PPP frame exchange order with reference to RFC documents. (include options)
    Analyze pppdump output to fit a frame format of PPP.
      LCP frames, IPCP frames and Data frame (IPv4).
      Both of default option and other options.
Example
pppd -detach crtscts lock debug noaccomp nopcomp asyncmap 0xffffffff record /root/test01 10.1.3.10:10.1.3.20 /dev/ttyS0 38400

## Slide 21: References
http://www.tldp.org/HOWTO/PPP-HOWTO/
http://linux.about.com/library/cmd/blcmdl8_pppdump.htm
RFC 1661, RFC 1662, RFC 1332
James Carlson, “PPP Design, Implementation, and Debugging 2nd edition,” Addison-Wesley, July 2000.